CM1001d-T

Architectural Specifications

The subwoofer shall consist of one 254 mm (10 in.) low-frequency transducer installed in a 12.9-liter ported enclosure. The transducer shall have a polypropylene cone with a butyl rubber surround. The speaker shall include a 150-watt transformer.

Performance specifications of a typical production unit shall be as follows: Usable frequency range shall extend from 41 Hz - 224 Hz, -10 dB. Maximum continuous output at 1 meter shall be at least 111 dB. The CM1001d-T subwoofer shall include a selectable 25-, 70.7-, 100-volt tap switch and transformer bypass position. Rated power capacity of the components and network shall be at least 150 watts continuous RMS and conform to EIA-426-B testing.

The backcan shall be constructed of galvanized steel with a UL 94 V(0) flame-rated ABS baffle. The grille shall be constructed of powder-coated steel. Packaged complete with UL-rated conduit cover plate, color-coded tile bridge (to match color-coded backcan label), grille, and paint shield, the integrated in-ceiling subwoofer is engineered for high performance and rapid installation in plenum spaces. The speaker incorporates a secondary attachment point for added security, or code satisfaction where required.

Installation for the speaker shall be by two-screw, blind-mount, constant-tension, fixed-winged assembly and shall attach to ceiling thicknesses ranging from 6.4 mm (0.25 in.) to 48.5 mm (1.91 in.). The external wiring input connector shall be a four-pin, 5.08 mm Euroblock for 4 ohm or distributed systems and shall accept from 10 – 22-gauge wire.

The unit is factory preset to the 150-watt setting in the 70.7-volt operating mode. with a tap switch located on the front baffle.

The system shall be the SoundTube CM1001d-T for low- and high-impedance applications.