CM500i

Architectural Specifications

The loudspeaker shall consist of a 133 mm (5.25 in.) low-frequency transducer and a 25 mm (1.0 in.) high-frequency transducer with a crossover network installed in the enclosure. The low-frequency voice coil diameter shall be 25 mm (1.0 in.).

Performance specifications of a typical production unit shall be as follows: Useable frequency response shall extend from 55 Hz – 22 kHz (-10 dB, half space). Measured sensitivity (2.83-volt input, 1 meter) shall be at least 86.5 dB. The speaker shall have a nominal impedance of 8 ohms. The speaker shall be available for 25-, 70.7- and 100-volt modes and shall include a six-position tap switch with a transformer bypass position. The frequency-dividing network shall have a crossover frequency of 3 kHz with slopes of 12 dB per octave (2nd order) for both low- and high-pass filters. Rated power capacity shall be at least 75 watts continuous (RMS) and conform to EIA-426-B testing. Maximum continuous output at 1 meter shall be 105.5 dB.

The low-frequency transducer shall have a polypropylene cone with rubber surround. The high-frequency transducer shall be constructed of titanium with a proprietary BroadBeam® waveguide.

Installation for the speaker shall be by two-screw, blind-mount, constant-tension winged assembly and shall attach to ceiling thicknesses ranging from 6.4 mm (0.25 in.) to 48.5 mm (1.91 in.). The fixed-wing assembly shall be constructed of steel. A secondary attachment point has been included on the back of the unit. The external wiring input connector shall be a four-pin, 5.08 mm Euroblock for 8 ohm or distributed systems and shall accept from 10 – 22-gauge wire.

The maximum backcan dimensions shall be no more than 197 mm (7.75 in.) in height by 219.2 mm (8.63 in.) in diameter. The maximum visible dimensions shall be no more than 24.4 mm (0.96 in.) in height by 271.9 mm (10.71 in.) in diameter. The backcan shall be constructed of aluminum.

The grille shall be constructed of an ABS bezel and powder-coated steel for lasting performance in the elements. The affixed grille and bezel shall be mounted to the speaker enclosure (backcan) via neodymium magnets and included safety leash. Also included are a paint mask for in-field painting and an installation aid that serves as a handhold during mounting.

The system shall include a 21-gauge galvanized steel support backing plate (tile bridge) to reinforce the ceiling material and tile support rails. The tile bridge shall be color-coded (blue) to simplify ordering and inventory tracking. The maximum tile bridge dimensions shall be no more than 600.1 mm (23.62 in.) in length by 323.9 mm (12.75 in.) in width and 11 mm (0.41 in.) in height with a 228.6 mm (9.0 in.) cutout for speaker mounting.

The unit has an optional color-coded (blue) pre-construction bracket (AC-CM5-PCB) that shall be compatible with an optional junction box (AC-CMi-JBOX). A 2-foot, 18-gauge wire whip and Euroblock connector shall be included with the junction box. The maximum dimensions of the pre-construction bracket shall be no more than 635 mm (25.0 in.) in length by 381 mm (15.0 in.) in width and 128 mm (5.0 in.) in height (includes affixed junction box) with a 228.6 mm (9.0 in.) cutout for speaker mounting.

The system shall be the SoundTube CM500i for both low- and high-impedance applications.