HP1290i

Architectural Specifications

The loudspeaker shall consist of one 305 mm (12.0 in.) low-frequency transducer and one 35 mm (1.375 in.) high-frequency transducer with a frequency-dividing network installed in a ported enclosure. The low-frequency voice coil diameter shall be 50 mm (2.0 in.).

Performance specifications of a typical production unit shall be as follows: Useable frequency range shall extend from 59 Hz - 22 kHz, -10 dB. The loudspeaker shall be available with selectable 25/70.7/100-volt tap switch with transformer bypass position. The frequency-dividing network shall have a crossover frequency of 2.2 kHz. Rated power capacity of the components and network shall be at least 150 watts continuous (RMS) and conform to EIA-426-B testing. Maximum continuous output at 1 meter shall be at least 118 dB.

The low-frequency transducer shall have treated fiber cone material with a treated cloth surround. The high-frequency transducer shall be constructed of Mylar material.

Installation for the speaker shall be by galzanized steel cable affixed to the speaker chasis via an integrated snap hook. For safety redundancy, a secondary steel cable shall be included. The external wiring input connector shall be a four-pin, 5.08 mm Euroblock for 8 ohm or distributed systems and shall accept 10-22-guage wire. The unit shall be for indoor and outdoor applications and have a weather-resistant boot covering all wire connections. The system shall ship complete with hanging hardware including hanging and safety cables, Euroblock connector and terminal weather boot. The speaker has an optional surface mount bracket (AC-RS-SM1290).

The ported enclosure shall be constructed from injection-molded, glass-reinforced ABS with a total volume of 2 cubic feet. The grille shall be constructed of powder-coated steel and affix to the speaker via friction fit with two blind-mounted, radial screws.

The unit is factory preset to the 150-watt setting in the 70.7-volt operating mode, with a tap switch located on the front baffle of the speaker, accessible by a removable grille plug. Signal input shall be by four-pin Euroblock connector, which accepts up to 10-gauge wire.

The system shall be the SoundTube HP1290i for both low- and high-impedance applications.